## Slide 1
Michael D. Dukes, Ph.D., P.E.
Agricultural & Biological Engineering
Institute of Food and Agricultural Sciences (IFAS)‏
Landscape Fundamentals IST
Wimauma, FL, Feb 10, 2009
Florida Landscape Irrigation Water Requirements
Notes: 1
Build Green & Profit
1

## Slide 2: Plant vs. Irrigation Water Requirement
Plant water requirement is the total water (rain+irrigation) required by the plants
Irrigation water requirement includes some estimate of rainfall for plant water needs
Both concepts infer well-watered (i.e. non-stressed) conditions
Notes: The plant water requirement accounts for all water inputs into the plant-soil system. The irrigation water requirement is the amount of irrigation needed to supplement rainfall to maintain acceptable yield and or quality. Both of these concepts imply well-watered conditions. “Well-watered” means that irrigation is applied when an allowable deficit occurs in the soil (not up to permanent wilting point as this level will typically cause permanent yield or quality reduction in many types of plants). However, irrigation is applied such that runoff and deep percolation of irrigation water below the root zone does not occur. The net irrigation water requirement is the actual amount of water needed in the root zone. The gross irrigation water requirement is the amount of water that must be pumped or diverted in an irrigation system to achieve the net irrigation amount in the target irrigation area. The gross irrigation water requirement is computed by dividing the net irrigation water requirement by the irrigation system efficiency.

## Slide 3: Turfgrass Plant Water Requirements
St. Augustine & bermudagrass, 43 inches/yr, S. Florida (Stewart and Mills, 1967)
Bahiagrass, 33 inches/yr, N. Florida (Jia et al., 2007)
Notes: These numbers are turfgrass ET demands with no rainfall input and the differences between the two studies are attributible to climate differences in South Florida (Ft. Lauderdale) vs. North Florida (Citra).
Stewart, E. H., and Mills, W. C. (1967). "Effect of Depth to Water Table and Plant Density on Evapotranspiration Rate in Southern Florida." Transactions of the ASAE, 10(6), 746-747.
Jia, X., Dukes, M. D., Jacobs, J. M. (2007). "Development of bahiagrass crop coefficient in a humid climate." Proc., International Meeting of the American Society of Agricultural and Biological Engineers, American Society of Agricultural and Biological Engineers, Minneapolis, MN, ASABE Paper No. 07-2151.

## Slide 4
Notes: Data above are for Jacksonville and represent 30 yr averages (1961-1990). Even during rainy periods, irrigation is required for shallow rooted crops/plants due to intermittent rainfall (see next slide). Turfgrass irrigation requirement here calculated with 50% MAD, 8 inch root zone, on a fine sand with about 6% water holding capacity.

## Slide 5: Timing is Everything!
Chart: Day of the Month (April 1961)
 | 0.32 | 0 | 0.23 | 0 | 0 | 0.09 | 0.19 | 0 | 1.31 | 0 | 0 | 0.48 | 0 | 0 | 1.32 | 0.22 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: Supplemental would likely have been needed the later part of this month and possibly within the first week due to the high evaporative demand during that time.

## Slide 6: Turfgrass Plant Water Requirements
St. Augustine & bermudagrass, 43 inches/yr, S. Florida (Stewart and Mills, 1967)
Bahiagrass, 33 inches/yr, N. Florida (Jia et al., 2007)
SWFWMD landscape coefficient for permitting study: similar water use for St. Augustine, Zoysia, and bahiagrass in first half year
Notes: Last bullet refers to SWFWMD funded study. To date (summer 2008), zoysia and bahia have similar ET rates. St. Aug was injured by frost and herbicide application spring 08 but rates have recently tracked well with the others. More results will be forthcoming.

## Slide 7: Turfgrass Irrigation Water Requirements - Range
Cardenas-Lailhacar (2008), no irrigation required on bermudagrass 2004-05
Davis (2008), reduced time schedule, 2 d/wk irrigation of ~22.5 inches/yr resulted in acceptable turf quality in a year with frequent dry periods (2006-07)
Notes: During the study in 2004 & 2005 on bermudagrass, good quality was found on all turf plots ranging from zero irrigation to levels in excess of ET demand. Rainfall during the testing period had fairly normal frequency and normal to above normal amounts (Cardenas-Lailhacar et al., 2008). Davis (2008) showed that a reduced schedule of 2 d/wk irrigation with a rain sensor resulted in adequate St. Augustinegrass quality in a dry year in Hillsborough County with a well-maintained irrigation system. Shedd et al. (2008) reported St. Augustinegrass decline below acceptable quality levels with 1 d/wk irrigation. In contrast, Peacock and Dudeck (1984) reported no difference in turfgrass quality when St. Augustinegrass was watered every 2, 3, 4, and 6 days. However, their study was conducted on a different site that likely had a shallow water table as compared to the deep sand in the Shedd et al. (2008) study. In addition, the Peacock and Dudeck (1984) study used hand watering ensuring perfect application uniformity; whereas, Shedd et al. (2008) used residential irrigation equipment.
Cardenas-Lailhacar, B., M.D. Dukes, and G.L. Miller. 2008. Sensor-based automation of irrigation on bermudagrass during wet weather conditions. J. Irrig. & Drainage Eng. 134(2):120-128.
Davis, S. 2008. Evapotranspiration-based irrigation controllers under dry conditions in Florida. ME Thesis.
Shedd, M., M.D. Dukes, and G.L. Miller. 2008. Effect of irrigation control on turfgrass quality and root growth. Florida State Horticultural Society Proceedings. In press.
Peacock, C.H. and A.E. Dudeck. 1984. Physiological response of St. Augustinegrass to irrigation scheduling. Agronomy Journal 76:275-279.

## Slide 8: Turfgrass Irrigation Water Requirements – Days of the Week
Shedd et al. (2008) showed that 1 d/wk irrigation on established St. Augustinegrass resulted in poor or reduced turfgrass quality during drought (spring 06 & 07)
Peacock and Dudeck (1984) reported good St. Augustinegrass quality for irrigation every 6 days
Notes: During the study in 2004 & 2005 on bermudagrass, good quality was found on all turf plots ranging from zero irrigation to levels in excess of ET demand. Rainfall during the testing period had fairly normal frequency and normal to above normal amounts (Cardenas-Lailhacar et al., 2008). Davis (2008) showed that a reduced schedule of 2 d/wk irrigation with a rain sensor resulted in adequate St. Augustinegrass quality in a dry year in Hillsborough County with a well-maintained irrigation system. Shedd et al. (2008) reported St. Augustinegrass decline below acceptable quality levels with 1 d/wk irrigation. In contrast, Peacock and Dudeck (1984) reported no difference in turfgrass quality when St. Augustinegrass was watered every 2, 3, 4, and 6 days. However, their study was conducted on a different site that likely had a shallow water table as compared to the deep sand in the Shedd et al. (2008) study. In addition, the Peacock and Dudeck (1984) study used hand watering ensuring perfect application uniformity; whereas, Shedd et al. (2008) used residential irrigation equipment.
Cardenas-Lailhacar, B., M.D. Dukes, and G.L. Miller. 2008. Sensor-based automation of irrigation on bermudagrass during wet weather conditions. J. Irrig. & Drainage Eng. 134(2):120-128.
Davis, S. 2008. Evapotranspiration-based irrigation controllers under dry conditions in Florida. ME Thesis.
Shedd, M., M.D. Dukes, and G.L. Miller. 2008. Effect of irrigation control on turfgrass quality and root growth. Florida State Horticultural Society Proceedings. In press.
Peacock, C.H. and A.E. Dudeck. 1984. Physiological response of St. Augustinegrass to irrigation scheduling. Agronomy Journal 76:275-279.

## Slide 9: References
Stewart, E. H., and Mills, W. C. (1967). "Effect of Depth to Water Table and Plant Density on Evapotranspiration Rate in Southern Florida." Transactions of the ASAE, 10(6), 746-747.
Jia, X., Dukes, M. D., Jacobs, J. M. (2007). "Development of bahiagrass crop coefficient in a humid climate." Proc., International Meeting of the American Society of Agricultural and Biological Engineers, American Society of Agricultural and Biological Engineers, Minneapolis, MN, ASABE Paper No. 07-2151.
Cardenas-Lailhacar, B., M.D. Dukes, and G.L. Miller. 2008. Sensor-based automation of irrigation on bermudagrass during wet weather conditions. J. Irrig. & Drainage Eng. 134(2):120-128.
Davis, S. 2008. Evapotranspiration-based irrigation controllers under dry conditions in Florida. ME Thesis.
Shedd, M., M.D. Dukes, and G.L. Miller. 2008. Effect of irrigation control on turfgrass quality and root growth. Florida State Horticultural Society Proceedings. In press.
Peacock, C.H. and A.E. Dudeck. 1984. Physiological response of St. Augustinegrass to irrigation scheduling. Agronomy Journal 76:275-279.